## Slide 1
HIGH ALTITUDE LONG ENDURANCE (HALE) UAVs
Sustainable Flight Through Integrated Solar, Propulsion and Atmospheric Simulation
Parth Patil (22BTRAS031)
Guide: Dr Amalesh Barai, JAIN University

## Slide 2
Introduction to HALE UAVs
Key Capabilities
Altitude: 18+ km in stratosphere
Endurance: Days to weeks
Zephyr S achieved 64-day record
Persistent surveillance capability
LEO communication relay role
Notable Platforms
NASA Helios
730 kg | 75 m span | AR 30.9
Airbus Zephyr S
53 kg | 25 m span | AR 24
KARI EAV-3
53 kg | 19.5 m span | AR 17.4

## Slide 3
The Core Engineering Challenge
Energy Balance: Solar power collected during day must sustain entire 24-hour cycle
BATTERY SOLUTION
Night Storage: 24 kWh
Required Mass: ~95 kg
Density: 250 Wh/kg
Status: Exceeds feasible weight
Impact: Design not practical
HYDROGEN FUEL CELL
Night Storage: 24 kWh
Required Mass: ~4.3 kg
Energy Density: 265 Wh/kg
Status: Practical & viable
Impact: Dramatic mass reduction

## Slide 4
Project Objectives & Scope
1
Solar Irradiance Modeling
24-hour prediction with cloud cover dynamics (kc = 0.0–1.0)
2
Propulsion Optimization
Mission-based motor-propeller selection using Dantsker methodology
3
Atmospheric Simulation
ISA implementation with energy balance validation at 20 km altitude

## Slide 5
Literature Survey: HALE Platform Configurations
Platform
Mass
Wingspan
Aspect Ratio
Endurance
Zephyr S
53 kg
25 m
24
25+ days
NASA Helios
730 kg
75 m
30.9
14+ hours
KARI EAV-3
53 kg
19.5 m
17.4
Stratospheric test
Present Design
~114 kg
32 m
~30
Target: 24+ hours

## Slide 6
Computational Methodology
Integration Pipeline
Atmosphere
Solar
Irradiance
Aerodynamics
Propulsion
Energy
Balance
Implemented Subsystems
Solar Irradiance: 24-hour continuous simulation with cloud cover parameter
Propulsion: Mission-based motor-propeller selection using Dantsker methodology
Atmospheric:
ISA implementation with mission profile integration

## Slide 7
Propulsion Optimization Results
Power Reduction
22.6%
1994 W → 1543 W
Cruise power reduction directly reduces storage requirements
Energy Margin
208.1%
27,893 Wh surplus
Total Solar: 41,297 Wh | Daylight: 14.4 hours
Optimal Configuration: HALE-Direct D80 motor + HALE-M 72×40 propeller
System Efficiency: 58.6%
Validated across mission profile
Reduces night-time storage demand from estimated 24 kWh baseline

## Slide 8
Aerodynamic Performance Analysis
Lift-to-Drag Ratio (L/D) at 20 km Altitude: 17.2
Altitude
20 km
Air Density
0.088 kg/m³
Aspect Ratio
~30
Cruise Speed
~12 m/s
Design Considerations
High aspect ratio wings minimize induced drag at low speed and altitude
Required L/D of 25–30 achieved through composite wing structure
Aeroelastic coupling critical for 32 m flexible wing design
Stratospheric air density (0.088 kg/m³) requires extreme efficiency

## Slide 9
Energy Storage & Solar Technologies
Solar Cell Technology
Triple-Junction GaAs
25–30% Efficiency
Current Standard for HALE
Emerging: Perovskite (2024)
44,000 W/kg specific power
20.1% efficiency
Transformative potential if manufacturing matures
Energy Storage Thresholds
Fuel Cells Preferred
Above 2.8 kWh demand
Lithium-Sulfur (Next Gen)
300–350 Wh/kg
Commercial adoption 2025+
Record: Zephyr S
64-day continuous flight
Hybrid battery + fuel cell architecture

## Slide 10
Key Findings & Conclusions
Technical Feasibility
Confirmed through implemented computational models
Power Optimization
22.6% reduction achieved via propulsion optimization
Energy Margin
208.1% surplus enables perpetual endurance capability
Storage Strategy
Hybrid fuel cell + battery essential for practical multi-day endurance

## Slide 11
Recommendations for Future Work
Multi-point optimization: Extend beyond cruise to climb, descent, loiter segments
High-fidelity CFD: Validation under low-Reynolds-number conditions (Re = 3×10⁵)
Aeroelastic analysis: Flutter analysis for 32 m flexible wings using advanced methods
Thermal modeling: Battery/avionics performance at stratospheric temperatures (−60°C)
Flight validation: Scaled demonstrator fabrication and altitude testing
Emerging technologies: Perovskite solar cells, solid-state batteries, supercapacitors

## Slide 12
Key Takeaway
Solar-powered HALE UAVs are technically feasible through integrated computational modeling. Strategic propulsion optimization and hybrid energy storage enable perpetual endurance capability.

## Slide 13
Thank You
Parth Patil (22BTRAS031)
Department of Aerospace Engineering
JAIN University, Bangalore
Guide: Dr Amalesh Barai