## Slide 1
HIGH ALTITUDE LONG ENDURANCE (HALE) UNMANNED AERIAL VEHICLES
Sustained Flight Through Renewable Energy
Parth Patil (22BTRAS031)
Under the guidance of Dr Amalesh Barai
Department of Aerospace Engineering, JAIN (Deemed-to-be University)
2025-2026

## Slide 2
Presentation Agenda
1
Project Motivation & Aims
2
Literature Review — Existing HALE UAVs
3
Design Requirements & Constraints
4
Conceptual Design Overview
5
Aerodynamic, Propulsion & Structural Design
6
Performance Analysis & Results
7
Stability, Trade-offs & Validation
8
Conclusions & Future Work

## Slide 3
Project Motivation & Aims
Why HALE UAV?
• Bridge gap between conventional aircraft and satellites
• Operate at altitudes above 18 km for days/weeks
• Enable persistent surveillance & communication relay
• Reduce reliance on expensive satellite infrastructure
Project Aim
Conceive, analyse, and assess a theoretically sound solar-powered HALE UAV achieving multi-week endurance with payload versatility and operational reliability.
Target: Continuous flight above 18 km for minimum 24 hours, with ambition for several days

## Slide 4
Project Objectives
Primary
Develop comprehensive conceptual design satisfying mission endurance, payload, and safety requirements
Literature Survey
Review existing solar UAVs: aerodynamic configs, materials, energy storage
Design Limitations
Assess energy-storage limits, low-Re aerodynamics, structural/fatigue constraints
Performance Evaluation
Predict endurance, energy budgets, and mission reliability via simulation
Design Improvements
Recommend modifications: propulsion optimisation, aeroelastic analysis
Energy Integration
Quantify renewable energy impact on endurance and reliability

## Slide 5
Literature Review — Key Existing HALE UAVs
Platform | Mass (kg) | Wingspan (m) | AR | Endurance
Zephyr S | 53 | 25 | 24 | 25+ days
Helios | 730 | 75 | 30 | 14+ hours
EAV-3 (KARI) | 53 | 19.5 | 17.4 | Stratospheric test
AtlantikSolar | 6.9 | — | — | 81 hours (world record)
Present Design | ~114 | 32 | ~30 | Target: 24+ hours
Key Insights:
• High-aspect-ratio monoplane configurations dominate (AR 17.4 to 30+)
• Triple-junction GaAs cells achieve 25–30% efficiency — practical upper bound

## Slide 6
Design Requirements & Constraints
Mission Requirements
• Altitude: 18–22 km (stratospheric)
• Endurance: Minimum 24 hours (target: multi-day)
• Cruise speed: ~80 km/h
• Payload: 5-10 kg for instruments & comms
Technical Constraints
• Low Reynolds number flows (10⁵–10⁶)
• Structural stiffness for flutter avoidance
• Energy storage for night-time operation
• Environmental: cloud, wind shear, temperature
Performance Targets
25-30
Lift-to-Drag Ratio
>18 km
Service Ceiling
>24 hrs
Endurance

## Slide 7
Conceptual Design Overview
Top-Level Design Approach
• High-aspect-ratio monoplane configuration
• Solar cells on wing & fuselage surfaces
• Hybrid energy: solar + batteries + fuel cell
• CFRP composite ultra-lightweight structure
• Distributed propulsion system
Configuration Choice
Monoplane with high aspect ratio selected over biplane, BWB, and joined-wing based on:
• Manufacturing simplicity
• Proven technology readiness
• Structural reliability
• Ground handling practicality
Selected Design Parameters
Wingspan: 32 m | Aspect Ratio: ~30 | Empty Weight: ~114 kg | Payload: 5-10 kg

## Slide 8
Aerodynamic Design
Wing Geometry
• Wingspan: 32 m
• Aspect Ratio: ~30
• Low-Reynolds-number airfoil selection
• High-lift, low-drag optimization
Key Considerations
• Low Re flows (10⁵–10⁶): viscous effects dominate
• Target L/D: 25-30
• Minimise induced drag with high AR
• CFD + analytical methods for validation
Configuration Comparison
Configuration | Pros | Cons
Monoplane | Simple, proven | Standard AR
Biplane | High payload | Interference drag
BWB | Higher L/D | Complexity
Joined-wing | AR ~40 possible | Structural complexity
30
Aspect Ratio

## Slide 9
Propulsion System
Hybrid Energy Architecture
Solar (Day)
~9 kW
Triple-junction GaAs cells
25-30% efficiency
Storage (Night)
~24 kWh
Hybrid battery + fuel cell
Cruise Power
~2 kW
Electrical power demand
Energy System Reasoning
• Fuel cells outperform batteries above 2.8 kWh demand [10]
• Night-time requirement (~23.9 kWh) makes pure batteries infeasible (~95 kg)
• Hydrogen fuel cell solution: ~1.44 kg H2 + ~3 kg system = ~4.3 kg total
• Propulsion optimisation (Dantsker et al.) could reduce power demand by 19%

## Slide 10
Structural Design
Material Selection: CFRP Composites
• Carbon-fibre reinforced polymers
• High stiffness-to-weight ratio
• Anisotropic tailoring for load paths
• Out-of-plane reinforcement for damage tolerance
Structural Analysis
• ANSYS Workbench for FEA
• Static deflection analysis
• Modal frequency analysis
• Flutter margin prediction
Estimated Weight Breakdown
Component | Mass (kg) | Notes
Airframe (structure) | ~22 | CFRP primary
Solar panels | ~15 | GaAs on wing/fuselage
Energy storage | ~5 | Fuel cell + H2
Avionics & systems | ~5 | Sensors, comms, etc.
Payload | 5-10 | Mission equipment
Total Empty | ~52 | Without payload
Max Takeoff | ~62 | With max payload

## Slide 11
Performance Analysis
>24 hrs
Endurance
18-22 km
Altitude
25-30
L/D Ratio
~80 km/h
Cruise Speed
Key Analysis Results
• Cruise power: ~2 kW electrical
• Solar power available: ~9 kW (triple-junction GaAs at 1,360 W/m2)
• Night-time energy storage: ~23.9 kWh for 12-hour dark period
• Altitude power penalty: ~3.5% power increase per km altitude gain
• Propulsion optimisation potential: 19% efficiency improvement

## Slide 12
Stability & Control
Stability Analysis
• Longitudinal & directional stability
• Static margin: minimum 5% MAC
• Reference (EAV-3): 28.4% SM at 31% MAC
• CG remains stable during flight
Control Surfaces
• Conventional tail arrangement
• Ailerons for roll control
• Elevator for pitch
• Rudder for yaw
• Larger deflections at low density
Flutter Analysis
High-aspect-ratio very flexible wings introduce significant aeroelastic coupling. Using Murua et al. [44] methodology: geometrically exact beam finite elements + Unsteady Vortex Lattice Method (UVLM) provides accurate flutter boundary prediction including wing-tail wake interference effects.

## Slide 13
Design Trade-offs & Decisions
Decision | Trade-off | Resolution
Aspect Ratio 30 | Manufacturing vs performance | Practical compromise for ground handling
Fuel cell over battery | Complexity vs mass | 95 kg battery vs 4.3 kg fuel cell system
Monoplane config | AR limit vs simplicity | Proven technology, lower risk
Solar cell type | Efficiency vs weight | GaAs 25-30% for optimal power
Critical Trade-off: Battery vs Fuel Cell
Night-time storage of ~23.9 kWh makes pure lithium-ion solution infeasible:
• Battery mass: ~95.7 kg at 250 Wh/kg
• Hydrogen system: ~4.3 kg total (1.44 kg H2 + tankage + BOP)
→ Fuel cell selected for multi-day endurance

## Slide 14
Results Summary
Parameter | Value | Status
Wingspan | 32 m | Design target met
Aspect Ratio | ~30 | Within literature range
Empty Weight | ~52 kg | Competitive with Zephyr S
Max Takeoff | ~62 kg | With max payload
Endurance | >24 hours | Target achieved
Altitude | 18-22 km | Stratospheric
L/D Ratio | 25-30 | Target achieved
Cruise Power | ~2 kW | Feasible
Solar Power | ~9 kW | Available at altitude
Night Storage | ~23.9 kWh | Fuel cell solution

## Slide 15
Validation & Limitations
Validated Conceptually
✓ Energy balance closure verified
✓ Power requirements realistic (~2 kW)
✓ Solar power adequate (~9 kW available)
✓ Fuel cell mass savings confirmed
✓ L/D targets achievable per EAV-3
Limitations & Future Validation Needed
⚠ No wind tunnel testing performed
⚠ No CFD high-fidelity validation
⚠ No flight testing
⚠ Aeroelastic effects modeled conceptually
⚠ Manufacturing defects not quantified
This is a CONCEPTUAL DESIGN study. Detailed computational modeling, prototype fabrication, and flight testing are recommended for validation.

## Slide 16
Conclusions
Objectives Achieved
✓ Comprehensive conceptual design developed
✓ Literature review expanded with recent developments
✓ Energy system feasibility confirmed
✓ Design parameters aligned with literature benchmarks
✓ Trade-offs analyzed and justified
Key Findings
• Solar-powered HALE UAV is technically feasible for multi-day endurance
• Hybrid energy storage (fuel cell) essential over pure batteries for night-time power
• Propulsion optimisation can reduce power demand by up to 19%
• High-aspect-ratio wings require careful aeroelastic analysis

## Slide 17
Future Work & Recommendations
Near-Term (Research)
• Detailed CFD and wind tunnel validation
• Composite wing segment testing
• Flutter boundary testing
• Energy management algorithm development
Long-Term (Development)
• Scaled demonstrator fabrication
• Flight testing validation
• Technology maturation
• Mission system integration
Emerging Technologies to Monitor
• Morphing wings for adaptive aerodynamics
• Solid-state batteries for improved energy density
• Ultra-light flexible solar arrays
• Supercapacitor hybrid storage (eliminating battery degradation)

## Slide 18
Key References
[1] Goraj et al. (1999). Design concept of a HALE UAV. Aircraft Design
[2] Goraj, Z. (2004). HALE UAV of a new generation. Bull. Polish Academy
[3] Romeo et al. (2004). HELIPLAT: Design & analysis. Journal of Aircraft
[4] Najafi, Y. (2011). Design of HALE Solar Powered UAV. SJSU MS Thesis
[10] Boukoberine et al. (2019). Energy storage for UAVs. J. Power Sources
[39] Oettershagen et al. (2017). AtlantikSolar UAV. J. Field Robotics
[40] Hwang et al. (2016). KARI EAV-3 aerodynamic design. Journal of Aircraft
[44] Murua et al. (2011). Stability of very flexible aircraft. AIAA

## Slide 19
Questions & Discussion
Thank You
Parth Patil | 22BTRAS031
Dr Amalesh Barai (Advisor)
JAIN (Deemed-to-be University), Department of Aerospace Engineering